Information for Tier II Form

SIC (Standard Industrial Classification) Code – The SIC Code of 4941 applies to PWS.  (See this Website for classifications:  http://www.melissadata.com/lookups/sic.asp.)

Dun & Bradstreet number (Financial Officer should have this number if the PWS is listed with Dun & Bradstreet, since this is a non-required business identifier; or enter the name, city & state of your PWS in the right-hand margin of the following Website if you are listed as a principal agent:  http://www.dnb.com/US/duns_update/).

Chlorine CAS (Chemical Abstract Service) number - The CAS number for chlorine gas is 7782-50-5.  For CAS numbers for other chemicals that you possibly have in storage/use at your facility which also have a TPQ (Threshold Planning Quantity that require reporting to local and state authorities at certain quantities), go to the following Website:  http://www.epa.gov/ceppo/caalist.html.  In the right margin, you’ll find the link to the “list of lists” of reportable chemicals, which you’ll find listed in alphabetical order if you scroll about half-way through the 105-page document.

For an easy link to help locate your LEPC (Local Emergency Planning Committee to whom you are required to annually report chlorine and other chemicals at threshold quantities, in conjunction with the Missouri Emergency Response Commission and your local fire department), use the same Website as above:  http://www.epa.gov/ceppo/caalist.html.  You’ll also find links for the RMP (Risk Management Plan for chlorine gas storage) and Natural Disaster preparedness sites at this Website.

The contact information for MERC (Missouri Emergency Response Commission for mailing in your Tier 2 Form each year by the March 1st deadline, for obtaining more Tier 2 Forms or for asking questions, is as follows:  Missouri State Emergency Response Commission, P.O. Box 3133, Jefferson City, Missouri 65102.  The telephone number is 800-780-1014.

Container Type:  150 lb. cylinder or 1-ton container

Pressure:  85 PSIG (at room temperature of 70◦ F)

Temperature:   70◦ F (if room is kept at this temperature)